Quality of Service (QoS) Monitoring of Cellular Mobile Voice Services-Eastern Region

[April 2016]

Content

Table of Contents

1. Background									2

2. What we measure									2

3. Findings										3-8

4. Remedies										9

5. Coverage Signal Strength	 Graphs			                                    10-59

6. Speech Quality Charts					                                    60-62

Background

In pursuance of Annexure D1 and D2 of the Cellular Mobile Licence of Telecommunication Operators, the user perspective of the quality of voice services are tested to ensure the compliance of Operators to the obligations on service quality to the user.

The report is based on findings on quality of service in Eastern Region from 1st April to 23rd April 2016 for all Operators except for Expresso due to technical challenges.

What we measure

As per the Cellular Mobile licence obligations, the QoS indicators and their respective threshold for compliance under assessment considering the user’s perspective are;

( Stand-alone Dedicated Control Channel (SDCCH) Congestion Rate

( Call Setup Time (CST)

( Call Congestion Rate

( Call Drop Rate (CDR)

( Call Completion Rate (CCR)

( Voice Call Audio Quality

( Coverage

Findings

The results for the district capitals within Eastern Region tested during the period are as below:

- Stand-alone Dedicated Control Channel (SDCCH) Congestion Rate

SDCCH Congestion is defined as the probability of failure of accessing a stand-alone dedicated control channel during call set up.

For analysis and calculations,

SDCCH Congestion Rate should be equal or less than one per cent (1%).

The results for the cities and towns tested in April are as below:

Table 1 Signalling Congestion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Abetifi | 0% | 0% | 0% | 0% | 0% |
| April | Akim Oda | 0% | 0% | 0% | 0% | 0% |
| April | Akim Swedru | 0% | 0% | 0% | 0% | 0% |
| April | Akropong | 0% | 0% | 0% | 0% | 0% |
| April | Asamankese | 0% | 0% | 0% | 0% | 0% |
| April | Asesewa | 0% | 0% | 0% | 0% | 0% |
| April | Atimpoku | 0% | 0% | 0% | 0% | No Network |
| April | Begoro | 0% | 0% | 0% | 0% | No Network |
| April | Donkorkrom | 0% | 0% | 0% | 0% | No Network |
| April | Kade | 0% | 0% | 0% | 0% | No Network |
| April | Koforidua | 0% | 0% | 0% | 0% | 0% |
| April | Kwabeng | 0% | 0% | 0% | 0% | 0% |
| April | Kyebi | 0% | 0% | 0% | 0% | No Network |
| April | Mpraeso | 0% | 0% | 0% | 0% | 0% |
| April | New Abirem | 0% | 0% | 0% | 0% | No Network |
| April | Nkawkaw | 0% | 0% | 0% | 0% | 0% |
| April | Nsawam | 0% | 0% | 0% | 0% | 0% |
| April | Odumase Krobo | 0% | 0% | 0% | 0% | 0% |
| April | Ofoase | 0% | 0% | 0% | 0% | No Network |
| April | Somanya | 0% | 0% | 0% | 0% | 0% |
| April | Suhum | 0% | 0% | 0% | 0% | 0% |

REMARK:

- All Operators were in compliance with the  signalling congestion threshold of less than 1 percent (1%) in the available District Capitals tested.

- Call Setup Time (CST)

Call Setup Time is the period of time elapsing from the sending of a complete destination address (target telephone number) to the setting up of a call to the receiving terminal;

– Moment when an alerting signal is sent to the called terminal

– Moment user presses the SEND button on the calling terminal

CST should be less than ten seconds (<10secs) in 95% of cases.

Table 2 Call Setup Time, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Abetifi | 8.32sec | 4.33sec | 6.44sec | 6.67sec | 19.73sec |
| April | Akim Oda | 7.08sec | 4.83sec | 6.3sec | 13.02sec | 4.14sec |
| April | Akim Swedru | 5.82sec | 2.29sec | 6.37sec | 5.48sec | 8.05sec |
| April | Akropong | 9.73sec | 4.8sec | 7.53sec | 11.91sec | 23.24sec |
| April | Asamankese | 7.31sec | 5.41sec | 9.72sec | 12.05sec | 14.54sec |
| April | Asesewa | 9.42sec | 3.96sec | 4.55sec | 7.15sec | 7.92sec |
| April | Atimpoku | 9.73sec | 3.86sec | 9.06sec | 15.32sec | No Network |
| April | Begoro | 8.07sec | 4.09sec | 6.17sec | 6.69sec | No Network |
| April | Donkorkrom | 5.85sec | 12.82sec | 5.95sec | 5.64sec | No Network |
| April | Kade | 8.68sec | 4.55sec | 13.06sec | 13.06sec | No Network |
| April | Koforidua | 10.3sec | 5.26sec | 6.69sec | 11.24sec | 8.51sec |
| April | Kwabeng | 6.03sec | 4.19sec | 6.36sec | 5.45sec | 19.86sec |
| April | Kyebi | 8.19sec | 4.71sec | 5.85sec | 5.09sec | No Network |
| April | Mpraeso | 7.99sec | 9.69sec | 4.82sec | 5.74sec | 7.82sec |
| April | New Abirem | 7.93sec | 6.02sec | 6.83sec | 11.63sec | No Network |
| April | Nkawkaw | 8.56sec | 5.07sec | 8.82sec | 11.32sec | 9.21sec |
| April | Nsawam | 7.73sec | 4.36sec | 24.74sec | 12.23sec | 7.91sec |
| April | Odumase Krobo | 10.04sec | 6.19sec | 9.05sec | 11.64sec | 8sec |
| April | Ofoase | 6.16sec | 4.72sec | 9.89sec | 6.82sec | No Network |
| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| April | Somanya | 8.63sec | 5.03sec | 6.00sec | 10.97sec | 8.44sec |
| April | Suhum | 8.61sec | 4.56sec | 5.58sec | 8.9sec | 17.71sec |

REMARKS:

- All Operators failed to meet the parameter threshold in at least one locality.

- Airtel and Glo had delayed Call Setup Time of 11.75sec and 11.04 sec respectively in the Eastern Region.

- MTN had Call Setup Time delays at Koforidua and Odumase Krobo.

- Vodafone had Call Setup Time delays at Donkorkrom.

- Tigo had Call Setup Time delays in Kade and Nsawam.

- Airtel had Call Setup Time delays at Akim Oda, Akropong, Asamankese, Atimpoku, Kade, Koforidua, New Aberim, Nkawkaw,Nsawam, Odumase Krobo and Somanya.

- Glo had Call Setup Time delays at Abetifi, Asamankese, Kwabeng and Suhum.

- Call Congestion Rate

Call Congestion Rate is the probability of failure of accessing a traffic channel during call setup;

Traffic Channel Congestion should be equal or less than one per cent (1%).

Table 3 Call Congestion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Abetifi | 0% | 0% | 0% | 0% | 0% |
| April | Akim Oda | 0% | 0% | 0% | 0% | 0% |
| April | Akim Swedru | 0% | 0% | 0% | 0% | 0% |
| April | Akropong | 0% | 0% | 0% | 0% | 0% |
| April | Asamankese | 0% | 0% | 0% | 0% | 0% |
| April | Asesewa | 0% | 0% | 0% | 0% | 0% |
| April | Atimpoku | 0% | 0% | 0% | 0% | No Network |
| April | Begoro | 0% | 0% | 0% | 0% | No Network |
| April | Donkorkrom | 0% | 0% | 0.018% | 0% | No Network |
| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| April | Kade | 0% | 0% | 0% | 0% | No Network |
| April | Koforidua | 0% | 0% | 0% | 0% | 0% |
| April | Kwabeng | 0% | 0% | 0.016% | 0% | 0% |
| April | Kyebi | 0% | 0% | 0% | 0% | No Network |
| April | Mpraeso | 0% | 0.019% | 0% | 0% | 0.019% |
| April | New Abirem | 0% | 0% | 0% | 0% | No Network |
| April | Nkawkaw | 0% | 0% | 0% | 0% | 0.01% |
| April | Nsawam | 0% | 0% | 0% | 0% | 0% |
| April | Odumase Krobo | 0% | 0% | 0% | 0% | 0% |
| April | Ofoase | 0% | 0% | 0% | 0% | No Network |
| April | Somanya | 0% | 0% | 0% | 0% | 0% |
| April | Suhum | 0% | 0% | 0% | 0% | 0% |

REMARK:

- All Operators were in compliance with the licence threshold of less than one percent (1%) in the available District Capitals tested.

- Call Drop Rate ( CDR)

Voice Call Drop Rate is the probability of a call terminating without any of the users’ will;

Call drop rate should be equal or less than three per cent (3%).

Table 4 Call Drop Rate Cellular, Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Abetifi | 0% | 0% | 0% | 0% | 0% |
| April | Akim Oda | 0% | 0% | 0% | 0% | 0% |
| April | Akim Swedru | 0% | 0% | 0% | 0% | 0% |
| April | Akropong | 0% | 0% | 0% | 0% | 0% |
| April | Asamankese | 0% | 0% | 0% | 0% | 0% |
| April | Asesewa | 0% | 0% | 0% | 0% | 0% |
| April | Atimpoku | 0% | 0% | 0% | 0% | No Network |
| April | Begoro | 0% | 0% | 0% | 0% | No Network |
| April | Donkorkrom | 0% | 0% | 0% | 0% | No Network |
| April | Kade | 0% | 0% | 0% | 0% | No Network |
| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| April | Koforidua | 0% | 0% | 0% | 0% | 0% |
| April | Kwabeng | 0% | 0% | 0% | 0% | 0% |
| April | Kyebi | 0% | 0% | 0% | 0% | No Network |
| April | Mpraeso | 0% | 0% | 0% | 0% | 0% |
| April | New Abirem | 0% | 0% | 0% | 0% | No Network |
| April | Nkawkaw | 0% | 0% | 0% | 0% | 0% |
| April | Nsawam | 0% | 0% | 0% | 0% | 0% |
| April | Odumase Krobo | 0% | 0% | 0% | 0% | 0% |
| April | Ofoase | 0% | 0% | 0% | 0% | No Network |
| April | Somanya | 0% | 0% | 0% | 0% | 0% |
| April | Suhum | 0% | 0% | 0% | 0% | 0% |

REMARK:

- All Operators  were in compliance with the Call Drop Rate licence threshold of less than three percent (3%) in the available District Capitals tested.

- Call Completion Rate ( CCR)

Call Completion Rate is defined as the probability that a call has, after being successfully set up, be maintained during a period of time and ending normally.

Call Completion Rate should be equal or better than seventy percent (70%).

Table 5 Call Completion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Abetifi | 100% | 100% | 100% | 100% | 78.46% |
| April | Akim Oda | 100% | 98.96% | 100% | 55.41% | 95.39% |
| April | Akim Swedru | 100% | 100% | 97.96% | 94.12% | 100% |
| April | Akropong | 98.63% | 98.70% | 98.67% | 98.67% | 72.41% |
| April | Asamankese | 96.20% | 100% | 100% | 78.79% | 89.29% |
| April | Asesewa | 100% | 100% | 100% | 100% | 78.46% |
| April | Atimpoku | 100% | 100% | 100% | 100% | No Network |
| April | Begoro | 100% | 100% | 100% | 100% | No Network |
| April | Donkorkrom | 100% | 82.89% | 98.21% | 100% | No Network |
| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| April | Kade | 100% | 100% | 98.82% | 59.29% | No Network |
| April | Koforidua | 98.96% | 98.96% | 96.95% | 98.82% | 89.67% |
| April | Kwabeng | 100% | 100% | 96.77% | 98.41% | 78.46% |
| April | Kyebi | 100% | 100% | 98.80% | 100% | No Network |
| April | Mpraeso | 92% | 98.08% | 100% | 100% | 94.23% |
| April | New Abirem | 100% | 100% | 100% | 94.64% | No Network |
| April | Nkawkaw | 100% | 100% | 100% | 98.02% | 90.74% |
| April | Nsawam | 97.40% | 100% | 93.67% | 95.06% | 83.72% |
| April | Odumase Krobo | 98.48% | 100% | 96.875% | 100% | 91.18% |
| April | Ofoase | 100% | 98.41% | 79.17% | 98.41% | No Network |
| April | Somanya | 97.87% | 94.50% | 100% | 100% | 94.19% |
| April | Suhum | 100% | 100% | 98.85% | 100% | 50% |

REMARKS:

- MTN, Vodafone and Tigo were in compliance with the Call Completion Rate licence threshold of less than seventy percent (70%) in the available District Capitals tested.

- Airtel failed the Call Completion Rate licence obligation at Akim Oda and Kade.

- Glo failed the Call Completion Rate licence obligation at Suhum.

- Voice Call Audio Quality

It is the perceptibility of the conversation during a call. Voice Call Audio Quality is measured by a parameter called the Mean Opinion Score (MOS) which categorizes speech samples in ranges from 0 to 5.

| Range | Colour Code | Rating |
| --- | --- | --- |
| [0 – 2.5) |  | Poor |
| [2.5 – 3.5) |  | Fair |
| [3.5 – 4.1) |  | Good |
| [4.1 – 5) |  | Excellent |

Table 5 Speech Quality Mean Opinion Score Eastern Region, April 2016

| Eastern | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- |
| MOS | 3.66 | 3.77 | 3.78 | 3.61 | 3.62 |

REMARK:

- All Operators were assessed to give GOOD speech quality.

REMEDIES

- The NCA has notified Operators of these findings and has directed all Operators to improve their coverage in some localities by November 2016.

- Glo has been sanctioned for the failure in Call Setup Time obligation in the Eastern Region.

- Airtel has been granted moratorium till July 31, 2016 to resolve the persistent Call Setup Time delays which has been acute since 2015.

APPENDICES

COVERAGE AND SPEECH MAPS

The Maps below show the coverage level and speech quality in the various towns where monitoring was performed. The coverage map is a combination of both 2G and 3G network signal strength. In each plot is a legend to indicate definitions of signal strength and quality range attain by operators during measurement. Coverage levels in green falls in the rage of -85dBm and above are considered good. Those between -85 and -95dBm are considered average and are indicated in yellow. The red samples represent worse coverage in the range of -95 to -110dBm. The black samples represent areas with no coverage. The speech quality was assessed with Mean Opinion Score (MOS) which ranges from 5 to 1.

APPENDIX I

COVERAGE AT ABETIFI

Fig 1.  MTN Coverage Map, Abetifi

Remarks: Good network coverage in Abetifi.

Fig 2. Vodafone Coverage Map, Abetifi

Remarks: Good network coverage, but improvement is required within the Township.

Fig 3. Tigo Network Coverage Map, Abetifi

Remarks: Poor network coverage across Abetifi with improvement needed at Presby University College and Abetifi SHS.

Fig 4. Airtel Coverage Map, Abetifi

Remarks: Fair network coverage across Abetifi which requires improvement.

Fig 5.Glo Coverage Map, Abetifi

Remarks: Poor network coverage at Abetifi; needs major improvement.

COVERAGE AT AKIM ODA

Fig 6. MTN Coverage Map, Akim Oda

Remarks: Good network coverage across Akim Oda

Fig 7. Vodafone Coverage Map, Akim Oda

Remarks: Good network coverage; however the Kade- Brofoyedru Road needs improvement

Fig 8. Tigo Coverage Map, Akim Oda

Remarks: Fair network coverage at Akim Oda, with major improvements needed at the DVLA office, PCG Presbytery Office and the Christ Apostolic Church

Fig 9. Airtel Coverage Map, Akim Oda

Remarks: Good network coverage across Akim Oda with improvements needed at the DVLA office and Christ Apostolic Church.

Fig 10. Glo Coverage Map, Akim Oda

Remarks: Good network coverage at Akim Oda, with poor coverage along the Community 6 road which requires improvement

COVERAGE AT AKIM SWEDRU

Fig 11. MTN Coverage Map, Akim Swedru

Remarks: Good network coverage across Akim Swedru

Fig 12. Vodafone Coverage Map, Akim Swedru

Remarks: Fair network coverage with improvements required at the Market area and on Akim Oda- Swedru Highway.

Fig 13. Tigo Coverage Map, Akim Swedru

Remarks: Good network coverage across Akim Swedru.

Fig 14. Airtel Coverage Map, Akim Swedru

Remarks: Poor network coverage across Akim Swedru; needs major improvement.

Fig 15. Glo Coverage Map, Akim Swedru

Remarks: Poor network coverage across Akim Swedru; with major improvements needed

COVERAGE AT AKROPONG

Fig 16.  MTN Coverage Map, Akropong

Remarks: Good network coverage within Akropong.

Fig 17. Vodafone Coverage Map, Akropong

Remarks: Good network coverage across Akropong. However coverage at areas near VIP Lodge and Mamfe is poor and need improvement.

Fig 18.  Tigo Coverage Map, Akropong

Remarks: Fair network coverage at Akropong with improvements needed at Bella Vista and around the Presby Church.

Fig 19. Airtel Coverage Map, Akropong

Remarks: Generally good network coverage across Akropong; however areas around Bella Vista and the Presby Church are poor and require improvement.

Fig 20. Glo Coverage Map, Akropong

Remarks: Poor network coverage across Akropong with major improvement needed at Bella Vista and close to Mount Sinai Secondary School.

COVERAGE AT ASAMANKESE

Fig 21. MTN Coverage Map, Asamankese

Remarks: Good network coverage across Asamankese.

Fig 22. Vodafone Coverage Map, Asamankese

Remarks: Good network coverage within the Township, however areas around Asumpa need improvement.

Fig 23. Tigo Coverage Map, Asamankese

Remarks: Good network coverage across Asamankese

Fig 24. Airtel Coverage Map, Asamankese

Remarks: Good network coverage in Asamankese.

Fig 25. Glo Coverage Map, Asamankese

Remarks: Good network coverage at Asamankese, except the patchy coverage around the Latter-Day Saints Church.

COVERAGE AT ASESEWA

Fig 26. MTN Coverage Map, Asesewa

Remarks: Good network coverage within Asesewa but areas towards Akokoma is poor and need improvement.

Fig 27. Vodafone Coverage Map, Asesewa

Remarks: Good network coverage at Asesewa, but road leading to Akokoma is poor and must be improved.

Fig 28. Tigo Coverage Map, Asesewa

Remarks: Good network coverage across Asesewa.

Fig 29. Airtel Coverage Map, Asesewa

Remarks: Good network coverage across Asesewa.

Fig 30. Glo Coverage Map, Asesewa

Remarks: Good network coverage in Asesewa.

COVERAGE AT ATIMPOKU

Fig 31. MTN Coverage Map, Atimpoku

Remarks: Good network coverage across Atimpoku.

Fig 32. Vodafone Coverage Map, Atimpoku

Remarks: Good network coverage at Atimpoku but needs improvement at Senchi.

Fig 33. Tigo Coverage Map, Atimpoku

Remarks: Good network coverage in Atimpoku, except Senchi which requires major improvement.

Fig 34. Airtel Coverage Map, Atimpoku

Remarks: Good network coverage but Senchi needs improvements.

*Glo had no service in Atimpoku at the time of the test

COVERAGE AT BEGORO

Fig 35. MTN Begoro Network Coverage Map

Remarks: Good network coverage across Begoro

Fig 36. Vodafone Coverage Map, Begoro

Remarks: Good network coverage across Begoro.

Fig 37. Tigo Coverage Map, Begoro

Remarks: Good network coverage across Begoro with improvement needed at places on the Begoro-Nsutama road.

Fig 38. Airtel Coverage Map, Begoro

Remarks: Poor network coverage in Begoro Township; especially around the Goil Fuel Station. Major improvement required.

* Glo had no service in Begoro at the time of the test

COVERAGE AT DONKORKROM

Fig 39. MTN Coverage Map, Donkorkrom

Remarks: Good network coverage across Donkorkrom

Fig 40. Vodafone Coverage Map, Donkorkrom

Remarks: Good network coverage across Donkorkrom.

Fig 41. Tigo Coverage Map, Donkorkrom

Remarks: Fair network coverage with improvements needed at Odonkawkrom and South of Donkorkrom

Fig 42. Airtel Coverage Map, Donkorkrom

Remarks: Fair network coverage across Donkorkrom; however areas near Odonkawkrom and South of Donkorkrom are poor and require major improvement.

*Glo had no service in Donkorkrom at the time of the test

COVERAGE AT KADE

Fig 43. MTN Coverage Map, Kade

Remarks: Good network coverage at Kade

Fig 44. Vodafone Coverage Map, Kade

Remarks: Good network coverage.

Fig 45. Tigo Coverage Map, Kade

Remarks: Good network coverage across Kade.

Fig 46. Airtel Coverage Map, Kade

Remarks: Good network coverage; but areas along the Oda-New Aberim road need improvement.

*Glo had no service in Kade at the time of the test

COVERAGE AT KOFORIDUA

Fig 47. MTN Coverage Map, Koforidua Metropolitan

Remarks: Good network coverage across Koforidua Metropolitan.

Fig 48. Vodafone Coverage Map, Koforidua Metropolitan

Remarks: Good network coverage across Koforidua Metropolitan.

Fig 49. Tigo Coverage Map, Koforidua Metropolitan

Remarks: Good network coverage across Koforidua

Fig 50. Airtel Coverage Map, Koforidua Metropolitan

Remarks: Good network coverage across Koforidua.

Fig 51. Glo Network Coverage Map, Koforidua Metropolitan

Remarks: Good network coverage across Koforidua Metro.

COVERAGE AT KWABENG

Fig 52. MTN Coverage Map, Kwabeng

Remarks: Good network coverage in Kwabeng.

Fig 53.Vodafone Coverage Map, Kwabeng

Remarks: Good network coverage at Kwabeng.

Fig 54. Tigo Coverage Map, Kwabeng

Remarks: Good network coverage across Kwabeng.

Fig 55. Airtel Coverage Map, Kwabeng

Remarks: Good network coverage across Kwabeng.

Fig 56. Glo Coverage Map, Kwabeng

Remarks: Poor network coverage across Kwabeng; especially at the Market Centre, Kwabeng Zongo and around the Community Football Field which require major improvement

COVERAGE AT KYEBI

Fig 57. MTN Coverage Map, Kyebi

Remarks: Good network coverage across Kyebi

Fig 58. Vodafone Coverage Map, Kyebi

Remarks: Good network coverage with improvement needed around the Lorry Station and College of Education.

Fig 59. Tigo Coverage Map, Kyebi

Remarks: Fair network coverage in Kyebi; needs improvement

Fig 60. Airtel Coverage Map, Kyebi

Remarks: Fair network coverage at Kyebi with improvement required at Abuakwa State College and around the Community Football Field.

COVERAGE AT MPRAESO

Fig 61. MTN Coverage Map, Mpraeso

Remarks: Network coverage in Mpraeso is good.

Fig 62. Vodafone Coverage Map, Mpraeso

Remarks: Poor network coverage at Mpraseo. Major improvements required

Fig 63. Tigo Coverage Map, Mpraeso

Remarks: Good network coverage across Mpraeso, except the poor spots on the Agogo-Mpraeso road which need improvement.

Fig 64. Airtel Coverage Map, Mpraeso

Remarks: Good network coverage across Mpraeso, except the bad spots on the Agogo-Mpraeso road which need improvement.

Fig 65. Glo Coverage Map, Mpraeso Network

Remarks: Good network coverage at Mpraeso.

COVERAGE AT NEW ABIREM

Fig 66. MTN Coverage Map, New Abirem

Remarks: Good network coverage across New Abirem

Fig 67. Vodafone Coverage Map, New Abirem

Remarks: Good network coverage with some fair spots which require improvement.

Fig 68. Tigo Coverage Map, New Abirem

Remarks: Good network coverage in New Abirem.

Fig 69. Airtel Coverage Map, New Abirem

Remarks: Good network coverage across New Abirem.

*Glo had no service in New Abirem at the time of the test

COVERAGE AT NKAWKAW

Figure 70. MTN Coverage Map, Nkawkaw

Remarks: Good network coverage at Nkawkaw

Fig 71. Vodafone Coverage Map, Nkawkaw

Remarks: Good network coverage; however areas around Odwenanoma and the Nkawkaw Bypass need improvement.

Fig 72. Tigo Coverage Map, Nkawkaw

Remarks: Poor network coverage; especially at the SDA church, Dumpong Rural Bank Ltd, the Church of Pentecost and Holy Family Hospital which requires major improvement.

Figure 73. Airtel Coverage Map, Nkawkaw

Remarks: Good network coverage in Nkawkaw.

Fig 74. Glo Coverage Map, Nkawkaw

Remarks: Good network coverage across Nkawkaw.

COVERAGE AT NSAWAM

Figure 75. MTN Coverage Map, Nsawam

Remarks: Good network coverage at Nsawam

Fig 76. Vodafone Coverage Map, Nsawam

Remarks: Good network coverage across Nsawam.

Fig 77. Tigo Coverage Map, Nsawam

Remarks: Good network coverage across Nsawam.

Fig 78. Airtel Coverage Map, Nsawam

Remarks: Good network coverage in Nsawam.

Fig 79. Glo Coverage Map, Nsawam

Remarks: Good network coverage across Nsawam.

COVERAGE AT ODUMASE KROBO

Fig 80. MTN Coverage Map, Odumase Krobo

Remarks: Good network coverage at Odumase Krobo.

Fig 81.Vodafone Coverage Map, Odumase Krobo

Remarks: Good network coverage across Krobo with fair spots which require improvement.

Fig 82. Tigo Coverage Map, Odumase Krobo

Remarks: Good network coverage across Odumase Krobo

Fig 83. Airtel Coverage Map, Odumase Krobo

Remarks: Good network coverage across Odumase Krobo; however some improvement is required around the Market area.

Fig 84. Glo Coverage Map, Odumase Krobo

Remarks: Fair network coverage across Odumase Krobo, with major improvements required.

COVERAGE AT OFOASE

Fig 85. MTN Coverage Map, Ofoase

Remarks: Good network coverage within Ofoase Township, but road leading to Brenasi needs improvement.

Fig 86. Vodafone Coverage Map, Ofoase

Remarks: Fair network coverage; especially areas around Ofusikuma which require improvement.

Fig 87. Tigo Coverage Map, Ofoase

Remarks: Poor network coverage across Ofoase. Major improvements required.

Fig 88. Airtel Coverage Map, Ofoase

Remarks: Good network coverage at Ofoase; however Ofusikuma requires improvement

*Glo had no service in Ofoase at the time of the test

COVERAGE AT SOMANYA

Fig 89. MTN Coverage Map, Somanya

Remarks: Good network coverage across Somanya

Fig 90. Vodafone Coverage Map, Somanya

Remarks: Good network coverage, except for some patchy areas which need improvement

Fig 91. Tigo Coverage Map, Somanya

Remarks: Fair network coverage across Somanya with poor coverage around the Presby Church and on the Adjekpo road which require improvement.

Fig 92. Airtel Coverage Map, Somanya

Remarks: Fair network within Somanya. Improvements will be required around the Presby Church and on the Adjekpo road.

Fig 93. Glo Coverage Map, Somanya

Remarks: Fair network coverage across Somanya, with improvement required at Rite FM, Holy Trinity International School and on the Adjeko road.

Fig 94. MTN Coverage Map, Suhum

Remarks: Good network coverage across Suhum

Fig 95. Vodafone Coverage Map, Suhum

Remarks: Good network coverage across Suhum.

Fig 96. Tigo Coverage Map, Suhum

Remarks: Fair network coverage at Suhum with improvement required at Suhum Post Office, Suhum Secondary School and the Children’s Hospital.

Fig 97. Airtel Coverage Map, Suhum

Remarks: Good network coverage across Suhum

Fig 98. Glo Coverage Map, Suhum

Remarks: Poor network coverage in Suhum which requires major improvements.

APPENDIX II

SPEECH QUALITY FOR OPERATORS

Fig.  99, MTN Speech Quality report in Eastern Region

Fig.  100, Vodafone Speech Quality report in Eastern Region

Fig.  101, Tigo Speech Quality report in Eastern Region

Fig.  102, Airtel Speech Quality report in Eastern Region

Fig.  103, Glo Speech Quality report in Eastern Region

# Text boxes

NATIONAL COMMUNICATIONS AUTHORITY

[Communications for Development]