Quality of Service (QoS) Monitoring of Cellular Mobile Voice Services-Volta Region

[April 2016]

Content

Table of Contents

1. Background									2

2. What we measure									2

3. Findings										3-8

4. Remedies										8

5. Coverage Signal Strength	 Graphs			                                    9-48

6. Speech Quality Charts					                                    48-50

Background

In pursuance of Annexure D1 and D2 of the Cellular Mobile Licence of Telecommunication Operators, the user perspective of the quality of voice services are tested to ensure the compliance of Operators to the obligations on service quality to the user.

The report is based on findings on quality of service in Volta Region from 6th April to 13th April 2016 for all Operators except Expresso due to technical challenges.

What we measure

As per the Cellular Mobile licence obligations, the QoS indicators and their respective threshold for compliance under assessment considering the user’s perspective are;

( Stand-alone Dedicated Control Channel (SDCCH) Congestion Rate

( Call Setup Time (CST)

( Call Congestion Rate

( Call Drop Rate (CDR)

( Call Completion Rate (CCR)

( Voice Call Audio Quality

( Coverage

Findings

The results for the district capitals within Volta Region tested during the period are as below:

- Stand-alone Dedicated Control Channel (SDCCH) Congestion Rate

SDCCH Congestion is defined as the probability of failure of accessing a stand-alone dedicated control channel during call set up.

For analysis and calculations,

SDCCH Congestion Rate should be equal or less than one per cent (1%).

The results for the cities and towns tested in April are as below:

Table 1 Signalling Congestion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Adidome | 0% | 0% | 0% | 0% | 0% |
| April | Akatsi | 0% | 0% | 0% | 0% | 0% |
| April | Dambai | 0% | 0% | 0% | 0% | No Network |
| April | Denu | 0% | 0% | 0% | 0% | No Network |
| April | Dzodze | 0% | 0% | 0% | 0% | 0% |
| April | Ho | 0% | 0% | 0% | 0% | 0% |
| April | Hohoe | 0% | 0% | 0% | 0% | No Network |
| April | Jasikan | 0% | 0% | 0% | 0% | No Network |
| April | Kadjebi | 0% | 0% | 0% | 0% | No Network |
| April | Keta | 0% | 0% | 0% | 0% | 0% |
| April | Kete Krachi | 0% | 0% | 0% | 0% | No Network |
| April | Kpando | 0% | 0% | 0% | 0% | No Network |
| April | Kpasa | 0% | 0% | 0% | 0% | No Network |
| April | Kpetoe | 0% | 0% | 0% | 0% | 0% |
| April | Kpeve | 0% | 0% | 0% | 0% | No Network |
| April | Nkonya Ahenkro | 0% | 0% | 0% | 0% | No Network |
| April | Nkwanta | 0% | 0% | 0% | 0% | No Network |
| April | Sogakope | 0% | 0% | 0% | 0% | No Network |

REMARK:

- All Operators were in compliance with the  signalling congestion threshold of less than 1 percent (1%) in the available District Capitals tested.

- Call Setup Time (CST)

Call Setup Time is the period of time elapsing from the sending of a complete destination address (target telephone number) to the setting up of a call to the receiving terminal;

– Moment when an alerting signal is sent to the called terminal

– Moment user presses the SEND button on the calling terminal

CST should be less than ten seconds (<10secs) in 95% of cases.

Table 2 Call Setup Time, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Adidome | 9.2Sec | 4.5Sec | 7.3Sec | 6.6Sec | 9.6Sec |
| April | Akatsi | 8.1Sec | 13.2Sec | 6.6Sec | 6.5Sec | 9.1Sec |
| April | Dambai | 6.3Sec | 3.0Sec | 6.7Sec | 5.2Sec | No Network |
| April | Denu | 7.4Sec | 12.2Sec | 6.1Sec | 15.Sec | No Network |
| April | Dzodze | 7.6Sec | 18.4Sec | 6.6Sec | 5.4Sec | 13.3Sec |
| April | Ho | 7.7Sec | 17Sec | 7.3Sec | 16.2Sec | 5.89Sec |
| April | Hohoe | 7.3Sec | 14.9Sec | 6.8Sec | 6.2Sec | No Network |
| April | Jasikan | 7.8Sec | 4.8Sec | 6.1Sec | 6.1Sec | No Network |
| April | Kadjebi | 6.1Sec | 7.9Sec | 6.5Sec | 5Sec | No Network |
| April | Keta | 7.2Sec | 8.7Sec | 6.7Sec | 5.5Sec | 28.6Sec |
| April | Kete Krachi | 4.5Sec | 16.8Sec | 8.8Sec | 6.9Sec | No Network |
| April | Kpando | 8.7Sec | 15Sec | 8Sec | 5.9Sec | No Network |
| April | Kpasa | 7.1Sec | 8.8Sec | 7Sec | 5.8Sec | No Network |
| April | Kpetoe | 6.3Sec | 17Sec | 6.7Sec | 6.1Sec | 28.0Sec |
| April | Kpeve | 5.9Sec | 2.7Sec | 6.9Sec | 4.8Sec | No Network |
| April | Nkonya Ahenkro | 4.4Sec | 14.5Sec | 7.5Sec | 4.7Sec | No Network |
| April | Nkwanta | 7.9Sec | 6.0Sec | 7.8Sec | 5.5Sec | No Network |
| April | Sogakope | 7.8Sec | 15.6Sec | 6.5Sec | 5.3Sec | No Network |

REMARKS:

- MTN and Tigo met the Call Setup Time licence obligation at all District Capitals tested.

- Vodafone had Call Setup Time delays at Akatsi, Denu, Dzodze, Ho, Hohoe, Kete Krachi, Kpando, Kpetoe, Nkonya Ahenkro and Sogakope.

- Airtel had Call Setup Time delays at Denu and Ho.

- Glo had Call Setup Time delays at Dzodze, Keta and Kpetoe.

- Call Congestion Rate

Call Congestion Rate is the probability of failure of accessing a traffic channel during call setup;

Traffic Channel Congestion should be equal or less than one per cent (1%).

Table 3 Call Congestion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Adidome | 0% | 0% | 0% | 0% | 0% |
| April | Akatsi | 0% | 5.6% | 0% | 0% | 0% |
| April | Dambai | 0% | 0% | 0% | 0% | No Network |
| April | Denu | 0% | 0% | 0% | 0% | No Network |
| April | Dzodze | 0% | 0% | 0% | 0% | 0% |
| April | Ho | 0% | 0% | 0% | 7.7% | 0% |
| April | Hohoe | 0% | 0% | 0% | 0% | No Network |
| April | Jasikan | 0% | 0% | 9.6% | 0% | No Network |
| April | Kadjebi | 0% | 0% | 0% | 0% | No Network |
| April | Keta | 0% | 0% | 0% | 0% | 0% |
| April | Kete Krachi | 0% | 0% | 0% | 0% | No Network |
| April | Kpando | 0% | 0% | 0% | 0% | No Network |
| April | Kpasa | 0% | 0% | 0% | 0% | No Network |
| April | Kpetoe | 0% | 0% | 0% | 0% | 0% |
| April | Kpeve | 0% | 0% | 0% | 0% | No Network |
| April | Nkonya Ahenkro | 0% | 0% | 0% | 0% | No Network |
| April | Nkwanta | 0% | 0% | 0% | 0% | No Network |
| April | Sogakope | 0% | 0% | 0% | 0% | No Network |

REMARKS:

- MTN was in compliance with the licence threshold of less than one percent (1%) in all available locations tested.

- Vodafone recorded high Call Congestion at Akatsi.

- Tigo recorded high Call Congestion at Jasikan.

- Airtel recorded high Call Congestion at Ho.

- Glo met the Call Congestion licence obligation at all available locations tested.

- Call Drop Rate ( CDR)

Voice Call Drop Rate is the probability of a call terminating without any of the users’ will;

Call drop rate should be equal or less than three per cent (3%).

Table 4 Call Drop Rate Cellular, Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Adidome | 0% | 0% | 0% | 0% | 0% |
| April | Akatsi | 0% | 0% | 0% | 0% | 0% |
| April | Dambai | 0% | 0% | 0% | 0% | No Network |
| April | Denu | 0% | 0% | 0% | 0% | No Network |
| April | Dzodze | 0% | 0% | 0% | 0% | 0% |
| April | Ho | 0% | 0% | 0% | 0% | 0% |
| April | Hohoe | 0% | 0% | 0% | 0% | No Network |
| April | Jasikan | 0% | 0% | 0% | 0% | No Network |
| April | Kadjebi | 0% | 0% | 0% | 0% | No Network |
| April | Keta | 0% | 0% | 0% | 0% | 0% |
| April | Kete Krachi | 0% | 0% | 0% | 0% | No Network |
| April | Kpando | 0% | 0% | 0% | 0% | No Network |
| April | Kpasa | 0% | 0% | 0% | 0% | No Network |
| April | Kpetoe | 0% | 0% | 0% | 0% | 0% |
| April | Kpeve | 0% | 0% | 0% | 0% | No Network |
| April | Nkonya Ahenkro | 0% | 0% | 0% | 0% | No Network |
| April | Nkwanta | 0% | 0% | 0% | 0% | No Network |
| April | Sogakope | 0% | 0% | 0% | 0% | No Network |

REMARK:

- All Operators  were in compliance with the Call Drop Rate licence threshold of less than three percent (3%) in the available District Capitals tested.

- Call Completion Rate ( CCR)

Call Completion Rate is defined as the probability that a call has, after being successfully set up, be maintained during a period of time and ending normally.

Call Completion Rate should be equal or better than seventy percent (70%).

Table 5 Call Completion Rate, Cellular Mobile Voice Service, April 2016

| Month | Town | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- | --- |
| April | Adidome | 97% | 95% | 100% | 100% | 55% |
| April | Akatsi | 82.0% | 87% | 100% | 100% | 74% |
| April | Dambai | 100% | 100% | 100% | 86% | No Network |
| April | Denu | 100% | 92% | 75% | 100% | No Network |
| April | Dzodze | 98.6% | 95% | 100% | 100% | 33% |
| April | Ho | 96% | 84% | 99% | 68% | 85% |
| April | Hohoe | 100% | 90% | 98% | 100% | No Network |
| April | Jasikan | 100% | 100% | 45% | 100% | No Network |
| April | Kadjebi | 100% | 100% | 96% | 98.1% | No Network |
| April | Keta | 100% | 98% | 100% | 100% | 14% |
| April | Kete Krachi | 96% | 88% | 100% | 93% | No Network |
| April | Kpando | 81.8% | 93% | 98% | 100% | No Network |
| April | Kpasa | 75% | 100% | 100% | 100% | No Network |
| April | Kpetoe | 97% | 84% | 100% | 100% | 6% |
| April | Kpeve | 100% | 100% | 98% | 97% | No Network |
| April | Nkonya Ahenkro | 100% | 75% | 97% | 100% | No Network |
| April | Nkwanta | 100% | 88% | 100% | 97% | No Network |
| April | Sogakope | 64% | 91% | 100% | 100% | No Network |

REMARKS:

- Vodafone met the Call Completion Rate licence threshold of less than seventy percent (70%) in the all available District Capitals tested.

- MTN failed the Call Completion Rate licence obligation at Sogakope.

- Tigo failed the Call Completion Rate licence obligation at Jasikan.

- Airtel failed the Call Completion Rate licence obligation at Ho.

- Glo failed the Call Completing Rate licence obligation at Adidome, Dzodze, Keta and Kpetoe.

- Voice Call Audio Quality

It is the perceptibility of the conversation during a call. Voice Call Audio Quality is measured by a parameter called the Mean Opinion Score (MOS) which categorizes speech samples in ranges from 0 to 5.

| Range | Colour Code | Rating |
| --- | --- | --- |
| [0 – 2.5) |  | Poor |
| [2.5 – 3.5) |  | Fair |
| [3.5 – 4.1) |  | Good |
| [4.1 – 5) |  | Excellent |

Table 5 Speech Quality Mean Opinion Score Volta Region, April 2016

| Volta | MTN | Vodafone | Tigo | Airtel | Glo |
| --- | --- | --- | --- | --- | --- |
| MOS | 3.55 | 3.81 | 2.90 | 3.50 | 3.55 |

REMARK:

- MTN, Vodafone, Airtel and Glo were assessed to give GOOD speech quality.

- Tigo was assessed to give FAIR speech quality.

REMEDIES

- The NCA has notified Operators of these findings and has directed all Operators to improve their coverage in some localities by August, 2016.

- Sanction imposed on Vodafone for failure in Call Setup Time in the Volta Region has been suspended pending resolution of outstanding issues.

- Glo has been sanctioned for the failure in Call Setup Time obligation in the Volta Region.

- Glo has been directed to improve its network coverage in the Volta Region.

APPENDICES

COVERAGE AND SPEECH MAPS

The Maps below show the coverage level and speech quality in the various towns where monitoring was performed. The coverage map is a combination of both 2G and 3G network signal strength. In each plot is a legend to indicate definitions of signal strength and quality range attained by operators during measurement. Coverage levels in green falls in the range of -85dBm and above are considered good. Those between -85 and -95dBm are considered average and are indicated in yellow. The red samples represent worse coverage in the range of -95 to -105dBm. The black samples represent areas with no coverage. The speech quality was assessed with Mean Opinion Score (MOS) which ranges from 5 to 1.

APPENDIX I

COVERAGE AT ADIDOME

Fig 1.  MTN Coverage Map, Adidome

Remarks: Fair network coverage, Improvement is required at Adidome market and Lorry Station

Fig 2.  Vodafone Coverage Map, Adidome

Remarks: Good network coverage across Adidome; but improvement required at Adidome Market Station.

Fig 3.  Tigo Coverage Map, Adidome

Remarks: Good network coverage across Adidome but coverage at Adidome SHS is poor and requires improvement.

Fig 4.  Airtel Coverage Map, Adidome

Remarks: Fair network coverage across Adidome, but improvement is needed at Adidome SHS and Main Lorry Station.

Fig 5.  Glo Coverage Map, Adidome

Remarks: Poor network coverage, which needs major improvement across the town.

COVERAGE AT AKATSI

Fig 6.  MTN Coverage Map, Akatsi

Remarks: Fair network coverage. Improvement is needed at the Vodafone Office area and the Old Market Circle

Fig 7.  Vodafone Coverage Map, Akatsi

Remarks: Fair network coverage at Akatsi with improvement needed at the Old & New Market Circle

Fig 8.  Tigo Coverage Map, Akatsi

Remarks: Good network coverage, but improvement is needed at Akatsi Training College.

Fig 9.  Airtel Coverage Map, Akatsi

Remarks: Good network coverage; however some improvement is required at the old Central Market and Akatsi Training College.

Fig 10.  Glo Coverage Map, Akatsi

Remarks: Fair network coverage across Akatsi, with improvements needed at Akatsi Training College.

COVERAGE AT DAMBAI

Fig 11.  MTN Coverage Map, Dambai

Remarks: Fair network coverage with improvements needed at the Dambai Ferry market and the Zongo Mosque Area.

Fig 12.  Vodafone Coverage Map, Dambai

Remarks: Good network yet improvements are needed at the Dambai Ferry Market and areas around the Zongo Mosque.

Fig 13.  Tigo Coverage Map, Dambai

Remarks: Good network coverage across Dambai; however improvements are needed at Dambai SHS and Ferry Site Market

Fig 14.  Airtel Coverage Map, Dambai

Remarks: Good network across Dambai yet improvements is needed at the Dambai SHS campus

*Glo had no service in Dambai at the time of the test

COVERAGE AT DENU

Fig 15.  MTN Coverage Map, Denu

Remarks: Good network coverage yet improvement is needed at the Lorry Station junction

Fig 16.  Vodafone Coverage Map, Denu

Remarks: Good network coverage yet improvement is needed at the Lorry Station Junction

Fig 17.  Vodafone Coverage Map, Denu

Remarks: Fair network coverage in Denu with major improvement needed especially at the Lorry Station Junction

Fig 18.  Airtel Coverage Map, Denu

Remarks: Good network coverage, but improvement is needed at the St. Charles Taxi Station.

*Glo had no service in Denu at the time of the test

COVERAGE AT DZODZE

Fig 19.  MTN Coverage Map, Dzodze

Remarks: Fair network coverage however major network improvement is needed at the Catholic School and Dzodze SHS environs

Fig 20.  Vodafone Coverage Map, Dzodze

Remarks: Fair network coverage; however major network improvement is needed at the Catholic School and Dzodze SHS environs.

Fig 21.  Tigo Coverage Map, Dzodze

Remarks: Good network coverage across Dzodze.

Fig 22.  Airtel Coverage Map, Dzodze

Remarks: Poor network coverage in Dzodze with major network improvement needed at the Market, Dzodze SHS and its environs.

Fig 23.  Glo Coverage Map, Dzodze

Remarks: Poor network coverage in Dzodze with major network improvement needed at the Market, Dzodze SHS and its environs.

COVERAGE AT HO

Fig 24.  MTN Coverage Map, Ho

Remarks: Good network coverage in Ho.

Fig 25. Vodafone Coverage Map, Ho

Remarks: Good network coverage in Ho.

Fig 26.  Tigo Coverage Map, Ho

Remarks: Good network coverage in Ho.

Fig 27.  Airtel Coverage Map, Ho

Remarks: Fair network coverage in Ho Metropolis with major improvement needed, especially around the Zongo.

Fig 28.  Glo Coverage Map, Ho

Remarks: Fair network coverage in Ho yet improvement is needed at the Central Business Town.

COVERAGE AT HOHOE

Fig 29.  MTN Coverage Map, Hohoe

Remarks: Good network coverage.

Fig 30.  Vodafone Coverage Map, Hohoe

Remarks: Good network coverage.

Fig 31.  Tigo Coverage Map, Hohoe

Remarks: Good network coverage with improvement needed around the SHS.

Fig 32.  Airtel Coverage Map, Hohoe

Remarks: Fair network coverage across Hohoe which needs improvement at the Hohoe Central Market, Bank of Ghana and Kokeri

*Glo had no service in Hohoe at the time of the test

COVERAGE AT JASIKAN

Fig 33.  MTN Coverage Map, Jasikan

Remarks: Good network coverage across Jasikan

Fig 34.  Vodafone Coverage Map, Jasikan

Remarks: Good network coverage across Jasikan except around the Jasikan SHS which need improvement.

Fig 35.  Tigo Coverage Map, Jasikan

Remarks: Good network coverage in Jasikan with improvement needed at the Okyerekrom and the Ghana Commercial Bank.

Fig 36.  Airtel Coverage Map, Jasikan

Remarks: Fair network coverage across Jasikan, however the main Lorry Station and places around the Police Station need improvement.

*Glo had no service in Jasikan at the time of the test

COVERAGE AT KETA

Fig 37.  MTN Coverage Map, Keta

Remarks: Good network coverage yet improvement is needed around the Keta Nursing School.

Fig 38.  Vodafone Coverage Map, Keta

Remarks: Good network coverage yet improvement is needed at Keta Nursing School and its environs.

Fig 39.  Tigo Coverage Map, Keta

Remarks: Good network coverage across Keta.

Fig 40.  Airtel Coverage Map, Keta

Remarks: Good network coverage yet improvement is needed at Keta Nursing School and its environs.

Fig 41.  Glo Coverage Map, Keta

Remarks: Fair network coverage in Keta; however areas around the SHS need improvement.

COVERAGE AT KETE KRACHI

Fig 42.  MTN Coverage Map, Kete Krachie

Remarks: Good network coverage across; however areas around the District Assembly need improvements.

Fig 43.  Vodafone Coverage Map, Kete Krachi

Remarks: Good network coverage yet some improvement is needed at the District Assembly area.

Fig 44.  Tigo Coverage Map, Kete Krachi

Remarks: Good network coverage yet improvement is needed at places around the District Assembly.

Fig 45.  Airtel Coverage Map, Kete Krachi

Remarks: Fair network coverage yet improvement is needed at Krachi SHS area

*Glo had no service in Kete Krachi at the time of the test

COVERAGE AT KADJEBI

Fig 46.  MTN Coverage Map, Kadjebi

Remarks: Good network coverage with some improvement needed at the Main Lorry Station.

Fig 47.  Vodafone Coverage Map, Kadjebi

Remarks: Good network coverage; yet improvement is needed at the Main Lorry Station and the Police Station area.

Fig 48.  Tigo Coverage Map, Kadjebi

Remarks: Fair network coverage, but areas around the Main Lorry Station and the Police Station need improvement

Fig 49.  Airtel Coverage Map, Kadjebi

Remarks: Poor network coverage across Kadjebi which need major improvement

*Glo had no service in Kadjebi at the time of the test

COVERAGE AT KPANDO

Fig 50.  MTN Coverage Map, Kpando

Remarks: Poor network coverage across Kpando with major improvements needed at the Central Market and around the Government Hospital.

Fig 51.  Vodafone Coverage Map, Kpando

Remarks: Fair network coverage; however the Central Market and the Government hospital need to be improved.

Fig 52.  Tigo Coverage Map, Kpando

Remarks: Good network coverage across Kpando

Fig 53.  Airtel Coverage Map, Kpando

Remarks: Fair network coverage, however improvements are needed at Kpando Zongo, Commercial Area and Kpando SHS.

*Glo had no service in Kpando at the time of the test

COVERAGE AT KPASA

Fig 54.  MTN Coverage Map, Kpasa

Remarks: Fair network coverage; however improvement is needed at Kpasa Youth Center area and around the Central Mosque.

Fig 55.  Vodafone Coverage Map, Kpasa

Remarks: Fair network coverage. However improvement is needed at Kpasa Youth Center area and the central mosque area.

Fig 56.  Tigo Coverage Map, Kpasa

Remarks: Fair network coverage in Kpasa; however major improvement is needed at the Youth Center and Central Mosque.

Fig 57.  Airtel Coverage Map, Kpasa

Remarks: Fair network coverage with major improvement needed at Kpasa Youth Center and the Central Mosque

*Glo had no service in Kpasa at the time of the test

COVERAGE AT KPETOE

Fig 58.  MTN Coverage Map, Kpetoe

Remarks: Fair network coverage with improvement needed at the CEPS Training School.

Fig 59.  Vodafone Coverage Map, Kpetoe

Remarks: Good network coverage yet improvement is needed at the CEPS Training School and the new District Assembly Area.

Fig 60.  Tigo Coverage Map, Kpetoe

Remarks: Good network coverage across Kpetoe.

Fig 61.  Airtel Coverage Map, Kpetoe

Remarks: Poor network coverage which requires major improvement at CEPS Training School and the New District Assembly area.

Fig 62.  Glo Coverage Map, Kpetoe

Remarks: Poor network coverage which requires major improvement.

COVERAGE AT KPEVE

Fig 63.  MTN Coverage Map, Kpeve

Remarks: Good network coverage across Kpeve.

Fig 64.  Vodafone Coverage Map, Kpeve

Remarks: Fair network coverage across Kpeve with major improvement needed

Fig 65.  Tigo Coverage Map, Kpeve

Remarks: Good network coverage across Kpeve.

Fig 66.  Airtel Coverage Map, Kpeve

Remarks: Poor network coverage across Kpeve, especially at areas around the Fire Service office. Major improvement required

*Glo had no service in Kpeve at the time of the test

COVERAGE AT NKONYA AHENKRO

Fig 67.  MTN Coverage Map, Nkonya Ahenkro

Remarks: Generally good network coverage but places around the Nkonya M/A JHS have poor coverage and require improvement.

Fig 68.  Vodafone Coverage Map, Nkonya Ahenkro

Remarks: Good network coverage in Nkonya with improvement needed around the Nkonya M/A JHS

Fig 69.  Tigo Coverage Map, Nkonya Ahenkro

Remarks: Good network coverage across Nkonya Ahenkro.

Fig 70.  Airtel Coverage Map, Nkonya Ahenkro

Remarks: Good network coverage yet improvement is needed at the District Assembly area

*Glo had no service in Nkonya Ahenkro at the time of the test

COVERAGE AT NKWANTA

Fig 71.  MTN Coverage Map, Nkwanta

Remarks: Good network coverage but improvement is needed at the ADB area close to the Main Station.

Fig 72.  Vodafone Coverage Map, Nkwanta

Remarks: Good network coverage across Nkwanta.

Fig 73.  Tigo Coverage Map, Nkwanta

Remarks: Poor network coverage. Major improvement is needed across Nkwanta.

Fig 74.  Airtel Coverage Map, Nkwanta

Remarks: Poor network coverage across Nkwanta; major improvement is needed.

*Glo had no service in Nkwanta at the time of the test

COVERAGE AT SOGAKOPE

Fig 75.  MTN Coverage Map, Sogakope

Remarks: Good network coverage within Sogakope Township.

Fig 76.  Vodafone Coverage Map, Sogakope

Remarks: Good network coverage within Sogakope Township yet minor network improvement is needed at the Trinity Spa and the District Assembly Office.

Fig 77.  Tigo Coverage Map, Sogakope

Remarks: Good network coverage across Sogakope.

Fig 78.  Airtel Coverage Map, Sogakope

Remarks: Fair network coverage yet improvement is needed at Sogakope Holy Trinity Spa and the District Assembly Area.

*Glo had no service in Sogakope at the time of the test

APPENDIX II

SPEECH QUALITY FOR OPERATORS

Fig 79.   MTN Speech Quality report in Volta Region

Fig 80.   Vodafone Speech Quality report in Volta Region

Fig 81.  Tigo Speech Quality report in Volta Region

Fig 82.   Airtel Speech Quality report in Volta Region

Fig 83.   Glo Speech Quality report in Volta Region

# Text boxes

NATIONAL COMMUNICATIONS AUTHORITY

[Communications for Development]