3G Coverage Assessment of Cellular Mobile Services- Western Region

[March 2016]

Table of Contents

1. Background									2

2. What we measure									2

3. Findings										2-3

4. Remedies										4

5. Coverage Signal Strength		                                                                       5-42

Background

In pursuance of obligations of the 3G Cellular Mobile Licence of Telecommunication Operators, the consumer perspective of the 3G Coverage status are tested to ensure the compliance of Operators to the obligations on 3G Coverage to the user.

The report is based on findings on 3G verification campaign in the Western Region from 1st March to 23rd March 2016 for all Operators except for Expresso due to technical challenges.

What we measure

As per the 3G Cellular Mobile licence obligations, 3G-locked mode coverage samples are collected to obtain on the average a signal strength measurement which is representative of the coverage situation in each of the District Capital that was driven.

The 3G Signal Strength and their respective threshold for compliance considering the user’s perspective are categorised as follows;

| Rating | 3G Signal Strength Range (dBm) |
| --- | --- |
| No 3G Coverage | -105>RSCP |
| Poor | –105≤ RSCP < -95 |
| Fair | –95≤ RSCP< –85 |
| Good | –85 ≤RSCP < –20 |

Findings

The results for the district capitals within Western Region tested during the period are as below:

Table 1: Coverage Signal strength, March, 2016

| DISTRICT CAPITAL | MTN | VODAFONE | TIGO | AIRTEL | GLO |
| --- | --- | --- | --- | --- | --- |
| AGONA NKWANTA | Fair | Good | Good | Good | Good |
| AKONTOMBRA | Good | Good | Good | Fair | No 3G Coverage |
| ASANKRAGUA | Good | Good | Good | Fair | No 3G Coverage |
| DISTRICT CAPITAL | MTN | VODAFONE | TIGO | AIRTEL | GLO |
| AXIM | Good | Fair | Fair | Fair | No 3G Coverage |
| BIBIANI | Fair | Fair | Good | Fair | No 3G Coverage |
| BODI | No 3G Coverage | Good | No 3G Coverage | No 3G Coverage | No 3G Coverage |
| BOGOSO | Good | Good | Fair | Fair | No 3G Coverage |
| DABOASE | Fair | Good | Good | Fair | No 3G Coverage |
| DADIESO | Good | Good | No 3G Coverage | No 3G Coverage | No 3G Coverage |
| ENCHI | Poor | Good | Good | Good | No 3G Coverage |
| ESSAM | Good | Fair | Good | Good | No 3G Coverage |
| HALF-ASSINI | Good | Good | Fair | Fair | No 3G Coverage |
| JUABOSO | Fair | Good | Good | Fair | No 3G Coverage |
| MPOHOR | Good | Good | Good | No 3G Coverage | No 3G Coverage |
| NKROFUL | Good | Good | No 3G Coverage | Good | No 3G Coverage |
| SEKONDI | Good | Good | Good | Good | Fair |
| SHAMA | Good | Good | Good | Good | Good |
| TARKWA | Good | Good | Good | Fair | No 3G Coverage |
| WASSA AKROPONG | Fair | Good | Good | Fair | No 3G Coverage |
| WIAWSO | Good | Fair | Fair | Fair | No 3G Coverage |

REMARKS:

- MTN had good 3G coverage in Akontombra, Asankragua, Axim, Bogoso, Dadieso, Essam, Half-Assini, Mpohor, Nkroful, Sekondi, Shama, Tarkwa and Wiawso

- MTN had fair 3G coverage in Agona Nkwanta, Bibiani, Daboase, Juaboso, Wassa Akropong

- MTN had poor and no coverage in Enchi and Bodi respectively.

- Vodafone had good 3G in Agona Nkwanta, Akontombra, Asankragua, Bodi, Bogoso, Dadieso, Half-Assini, Mpohor, Nkroful, Sekondi, Shama, Tarkwa and Wassa Akropong

- Vodafone had fair 3G coverage in Axim, Bibiani, Essam and Wiawso

- Tigo had good 3G coverage in Agona Nkwanta, Akontombra, Asankragua, Bibiani, Daboase, Enchi, Essam, Juaboso, Mpohor, Sekondi, Shama, Tarkwa and Wassa Akropong

- Tigo had fair 3G coverage in Axim, Bogoso, Half-Assini and Wiawso.

- Tigo had no 3G coverage in Bodi, Dadieso and Nkroful.

- Airtel had good 3G coverage in Agona Nkwanta, Enchi, Essam, Nkroful, Sekondi and Shama

- Airtel had fair 3G coverage in Akontombra, Asankragua, Axim, Bibiani, Bogoso, Daboase, Half-Assini, Juaboso, Tarkwa, Wassa Akropong and Wiawso.

- Airtel had no 3G coverage in Bodi, Dadieso and Mpohor.

- Glo had good coverage in Shama and Agona Nkwanta

- Glo had fair coverage in Sekondi

- Glo had no 3G Coverage in Akontombra, Asankragua, Axim, Bibiani, Bodi, Bogoso, Daboase, Dadieso, Enchi, Essam, Mpohor, Half -Assini, Juaboso, Nkroful, Tarkwa, Wassa Akropong and Wiawso.

Remedies

- Tigo has been sanctioned for failing to maintain coverage at Nkroful.

- All operators were given a deadline of 31st December 2016 to provide 3G coverage in the new District Capitals that were drive-tested.

- All operators were directed to improve  their existing 3G coverage by 31st July 2016, even in localities where coverage was rated “Good”

APPENDICES

Coverage Signal Strength

The Maps below show the coverage level in District Capitals of the Western Region where monitoring was performed. The coverage map is based on the 3G network signal strength when tested in an idle mode. In each plot is a legend to indicate the signal strength and quality range attained by Operators during measurement.

Coverage levels in green falls in the range of -85dBm and above, and are considered good. Those between -85 and -95dBm are considered average or fair and are indicated in yellow. The red samples represent worse or poor coverage in the range of -95 to -105dBm. The black samples represent areas with no 3G coverage.

Coverage Legend

| Colour | Area Coverage Rating |
| --- | --- |
|  | Good Coverage Areas |
|  | Fair Coverage Areas |
|  | Poor Coverage Areas |
|  | Non-Existent Coverage Areas |

APPENDIX I

COVERAGE AT AGONA NKWANTA

Fig.  1 – MTN 3G Coverage Map, Agona Nkwanta – March 2016

Remarks: Good 3G coverage in Agona Nkwanta however improvements needed.

Fig.  2 – Vodafone 3G Coverage Map, Agona Nkwanta - March 2016

Remarks: Good 3G coverage in Agona Nkwanta

Fig.  3 – Tigo 3G Coverage Map, Agona Nkwanta- March 2016

Remarks: Good 3G coverage in Agona Nkwanta

Fig.  4 – Airtel 3G Coverage Map, Agona Nkwanta - March 2016

Remarks: Good 3G coverage in Agona Nkwanta

Fig.  5 – Glo 3G Coverage Map, Agona Nkwanta - March 2016

Remarks: Good 3G coverage in Agona Nkwanta however improvement is required

COVERAGE AT AKONTOMMBRA

Fig.  6 - MTN 3G Coverage Map, Akontombra - March 2016

Remarks: Good 3G coverage in Akontombra.

Fig.  7 - Vodafone 3G Coverage Map, Akontombra - March 2016

Remarks: Good 3G coverage in Akontombra however improvement is required.

Fig.  8 - Tigo 3G Coverage Map, Akontombra - March 2016

Remarks: Good 3G coverage in Akontombra however improvement is required.

Fig.  9 - Airtel 3G Coverage Map, Akontombra - March 2016

Remarks: Fair 3G coverage in and around Akontombra that needs to be improved.

COVERAGE AT ASANKRAGUA

Fig.  10 – MTN 3G Coverage Map, Asankragua - March 2016

Remarks: Fair 3G coverage in Asankragua which needs to be improved

Fig.  11- Vodafone 3G Coverage Map, Asankragua - March 2016

Remarks: Good 3G coverage in Asankragua

Fig.  12- Airtel 3G Coverage Map, Asankragua - March 2016

Remarks: Fair 3G coverage Asankragua however improvement is required

COVERAGE AT AXIM

Fig. 13 - MTN 3G Coverage Map, Axim- March 2016

Remarks: Fair 3G coverage in Axim which needs to be improved

Fig.  14 - Vodafone 3G Coverage Map, Axim- March 2016

Remarks: Fair 3G coverage in and around Axim which needs to be improved

Fig.  15 - Tigo 3G Coverage Map, Axim- March 2016

Remarks: Fair 3G coverage in and around Axim which needs to be improved

Fig.  16 – Airtel 3G Coverage Map, Axim- March 2016

Remarks: Fair 3G coverage in and around Axim that needs to be improved

COVERAGE AT BIBIANI

Fig. 17- MTN 3G Coverage Map, Bibiani - March 2016

Remarks: Fair 3G coverage in and around Bibiani which needs to be improved

Fig. 18 - Vodafone 3G Coverage Map, Bibiani - March 2016

Remarks: Fair 3G coverage in and around Bibiani which needs to be improved.

Fig. 19 - Tigo 3G Coverage Map, Bibiani - March 2016

Remarks: Good 3G coverage in Bibiani

Fig. 20 - Airtel 3G Coverage Map, Bibiani - March 2016

Remarks: Poor 3G coverage in and around Bibiani. A major improvement is required

COVERAGE AT BODI

Fig.  21 - Vodafone 3G Coverage Map, Bodi - March 2016

Remarks:  Good 3G coverage in Bodi

COVERAGE AT BOGOSO

Fig.  22 - MTN 3G Coverage Map, Bogoso - March 2016

Remarks: Good 3G coverage in Bogoso

Fig.  23- Vodafone 3G Coverage Map, Bogoso - March 2016

Remarks: Good 3G coverage in Bogoso

Fig.  24 – Tigo 3G Coverage Map, Bogoso - March 2016

Remarks: Fair 3G coverage in and around Bogoso which needs to be improved

Fig.  25 - Airtel 3G Coverage Map, Bogoso - March 2016

Remarks: Fair 3G coverage in and around Bogoso that needs to be improved

COVERAGE AT DABOASE

Fig.  26 - MTN 3G Coverage Map, Daboase - March 2016

Remarks: Fair 3G coverage in Daboase that needs to be improved

Fig.  27- Vodafone 3G Coverage Map, Daboase - March 2016

Remarks: Good 3G coverage Daboase however improvements are required

Fig.  28 - Tigo 3G Coverage Map, Daboase - March 2016

Remarks: Good 3G coverage in Daboase however improvement is required

Fig.  29 – Airtel 3G Coverage Map, Daboase - March 2016

Remarks: Fair 3G coverage in and around Daboase that needs to be improved

COVERAGE AT DADIESO

Fig.  30 - MTN 3G Coverage Map, Dadieso – March 2016

Remarks: Good 3G coverage in Dadieso

Fig.  31 - Vodafone 3G Coverage Map, Dadieso – March 2016

Remarks: Good 3G coverage in Dadieso

COVERAGE AT ENCHI

Fig.  32 - MTN 3G Coverage Map, Enchi - March 2016

Remarks: Poor 3G coverage in Enchi. A major improvement is needed

Fig.  33 - Vodafone 3G Coverage Map, Enchi - March 2016

Remarks: Good 3G coverage in Enchi

Fig.  34 - Tigo 3G Coverage Map, Enchi - March 2016

Remarks: Good 3G coverage in Enchi

Fig.  35- Airtel 3G Coverage Map, Enchi - March 2016

Remarks: Good 3G coverage in Enchi

COVERAGE AT ESSAM

Fig. 36   - MTN 3G Coverage Map, Essam - March 2016

Remarks: Good 3G coverage in Essam

Fig. 37 - Vodafone 3G Coverage Map, Essam - March 2016

Remarks: Fair 3G coverage in Essam which needs to be improved

Fig. 38 - Tigo 3G Coverage Map, Essam - March 2016

Remarks: Good 3G coverage in Essam however improvement is required

Fig.  39 - Airtel 3G Coverage Map, Essam - March 2016

Remarks: Poor 3G coverage in and around Essam. A major improvement is required

COVERAGE AT HALF-ASSINI

Fig. 40 - MTN 3G Coverage Map, Half Assini – March 2016

Remarks: Good 3G coverage in Half-Assini

Fig.  41 - Vodafone 3G Coverage Map, Half Assini – March 2016

Remarks: Fair 3G coverage in and around Half – Assini which needs to be improved

Fig.  42 - Tigo 3G Coverage Map, Half Assini – March 2016

Remarks: Fair 3G coverage in and around Half – Assini which needs to be improved

Fig.  41 - Airtel 3G Coverage Map, Half Assini – March 2016

Remarks: Fair 3G coverage in and around Half – Assini that needs to be improved

COVERAGE AT JUABOSO

Fig.  43 - MTN 3G Coverage Map, Juaboso - March 2016

Remarks: Fair 3G coverage in Juaboso which needs to be improved

Fig.  44 - Vodafone 3G Coverage Map, Juaboso - March 2016

Remarks: Good 3G coverage in Juaboso

Fig.  45 - Tigo 3G Coverage Map, Juaboso - March 2016

Remarks: Good 3G coverage in Juaboso however improvement is required

Fig.  46 - Airtel 3G Coverage Map, Juaboso - March 2016

Remarks: Fair 3G coverage in and around Juaboso that needs to be improved

COVERAGE AT MPOHOR

Fig.  47 - MTN 3G Coverage Map, Mpohor – March 2016

Remarks: Fair 3G coverage in Mpohor which needs to be improved

Fig.  49 – Tigo 3G Coverage Map, Mpohor – March 2016

Remarks:    Good 3G Coverage in Mpohor

COVERAGE AT NKROFUL

Fig.  50 - MTN 3G Coverage Map, Nkroful – March 2016

Remarks: Good 3G coverage in Nkroful

Fig.  51- Vodafone 3G Coverage Map, Nkroful – March 2016

Remarks: Good 3G coverage in Nkroful

Fig.  52- Airtel 3G Coverage Map, Nkroful – March 2016

Remarks: Fair 3G coverage in and around Nkroful that needs to be improved

COVERAGE AT SEKONDI

Fig.  53 - MTN 3G Coverage Map, Sekondi– March 2016

Remarks: Fair 3G coverage in and around Sekondi which needs to be improved

Fig.  54- Vodafone 3G Coverage Map, Sekondi– March 2016

Remarks: Good 3G coverage in Sekondi

Fig.  55– Tigo 3G Coverage Map, Sekondi– March 2016

Remarks: Good 3G coverage in Sekondi

Fig.  56 - Airtel 3G Coverage Map, Sekondi– March 2016

Remarks: Good 3G coverage in Sekondi

Fig.  57 - Glo 3G Coverage Map, Sekondi– March 2016

Remarks: Fair 3G coverage in and around Sekondi which needs to be improved

COVERAGE AT SHAMA

Fig.  58 - MTN 3G Coverage Map, Shama– March 2016

Remarks: Good 3G coverage in Shama

Fig.  59- Vodafone 3G Coverage Map, Shama– March 2016

Remarks: Good 3G coverage in Shama however improvement is needed

Fig.  60 – Tigo 3G Coverage Map, Shama– March 2016

Remarks: Good 3G coverage in Shama

Fig.  61 - Airtel 3G Coverage Map, Shama– March 2016

Remarks: Good 3G coverage in Shama

Fig.  62 - Glo 3G Coverage Map, Shama– March 2016

Remarks: Good 3G coverage in Shama however improvement is required

COVERAGE AT TARKWA

Fig.  63 - MTN 3G Coverage Map, Tarkwa– March 2016

Remarks: Good 3G coverage in Tarkwa

Fig.  64- Vodafone 3G Coverage Map, Tarkwa– March 2016

Remarks: Good 3G coverage in Tarkwa

Fig.  65 – Tigo 3G Coverage Map, Tarkwa– March 2016

Remarks: Fair 3G coverage in Tarkwa which needs to be improved

Fig.  66 - Airtel 3G Coverage Map, Tarkwa– March 2016

Remarks: Fair 3G coverage in Tarkwa which needs to be improved

COVERAGE AT WASSA AKROPONG

Fig.  67 - MTN 3G Coverage Map, Wassa Akropong– March 2016

Remarks: Fair 3G coverage in Wassa Akropong which needs improvement

Fig.  68- Vodafone 3G Coverage Map, Wassa Akropong– March 2016

Remarks: Good 3G coverage in Wassa Akropong

Fig.  69 – Tigo 3G Coverage Map, Wassa Akropong– March 2016

Remarks: Good 3G coverage in Wassa Akropong however improvements needed

Fig.  70 - Airtel 3G Coverage Map, Wassa Akropong– March 2016

Remarks: Fair 3G coverage in and around Wassa Akropong that needs to be improved

COVERAGE AT WIAWSO

Fig.  71 - MTN 3G Coverage Map, Wiawso– March 2016

Remarks: Good 3G coverage in Wiawso

Fig.  72- Vodafone 3G Coverage Map, Wiawso– March 2016

Remarks: Fair 3G coverage in Wiawso however improvement is needed

Fig.  73 – Tigo 3G Coverage Map, Wiawso– March 2016

Remarks: Fair 3G coverage in and around Wiawso which needs to be improved

Fig.  74 - Airtel 3G Coverage Map, Wiawso– March 2016

Remarks: Poor 3G coverage in and around Wiawso. A major improvement needed

APPENDIX II

RSCP SAMPLING DISTRIBUTION

Fig.  75 - MTN 3G Coverage Samples Plot in the Western Region

Remarks: MTN recorded its highest count of RSCP samples in the range –85 ≤RSCP < –20 dBm; representing “Good” coverage across most of the district areas tested.

Fig.  77 - Vodafone 3G Coverage Samples Plot in the Western Region

Remarks: Vodafone recorded its highest count of RSCP samples in the range –85 ≤RSCP < –20 dBm; representing “Good” coverage across most of the district areas tested.

Fig.  78 - Tigo 3G Coverage Samples Plot in the Western Region

Remarks: Tigo recorded its highest count of RSCP samples in the range –85 ≤RSCP < –20 dBm; representing “Good” coverage across most of the district areas tested.

Fig.  79 - Airtel 3G Coverage Samples Plot in the Western Region

Remarks: AIRTEL recorded its highest count of RSCP samples in the range –85 ≤RSCP < –20 dBm; representing “Good” coverage across most of the district areas tested.

Fig.  80 - Glo 3G Coverage Samples Plot in the Western Region

Remarks: GLO recorded its highest count of RSCP samples in the range –105> RSCP dBm, representing “No 3G Coverage” across most of the district areas tested

# Text boxes

NATIONAL COMMUNICATIONS AUTHORITY

[Communications for Development]